Complete (

# Concrete Curb and Gutter     -Inch      Type

SPV.0090.

905-_____-_____

#### Buy America

Certification documents for steel reinforcement items must denote compliance to all elements of Buy America provisions

See Item of Concrete

- Assign 905-____-____

Concrete

- Diary entry required.  Bid Item ID: _______________

  - Strength evaluation test results required

Tie Bars

Steel

- Diary entry required.  Bid Item ID: _______________

  - Certified report of test and analysis are required

  - Buy America compliance from manufacturer is required

Epoxy

- Diary entry required.  Bid Item ID: _______________

  - Certified report of test and analysis are required

  - Buy America compliance from manufacturer is required

  - Verify manufacturer is on the approved list

Joint Filler

- Diary entry required.  Bid Item ID: _______________

| Item No. | Description | Plan Quantity | Final Quantity |
| --- | --- | --- | --- |
| SPV.0090. | Concrete Curb and Gutter 30-Inch SHES Type A | LF | LF |