Complete (

# Cross Stitching Longitudinal Cracks

SPV.0060.

905-_____-_____

#### Buy America

Certification documents for steel reinforcement items must denote compliance to all elements of Buy America provisions.

Tie Bar

Steel

- Diary entry required.  Bid Item ID: _______________

  - Accept in accordance with CMM 8-50 Exhibit 1, Concrete Reinforcement, Tie Bars

  - Certified report of test or analysis required for all heat numbers

  - Document all heat numbers

Epoxy Coating

- Diary entry required.  Bid Item ID: _______________

  - Verify product and manufacturer are on approved list:

    - Structures » Epoxy reinforcement coatings

  - Coating manufacturer’s certification of compliance is required

  - Applicator’s certification of compliance or certified report of test or analysis is required

  - Record all batch/lot numbers

Epoxy/Acrylic Grout for Anchoring

- Diary entry required.  Bid Item ID: _______________

  - Manufacturer’s certification of compliance is required

  - Certified report of test or analysis from testing laboratory is required

  - Verify temperature class and compressive strength cure times

| Item No. | Description | Plan Quantity | Final Quantity |
| --- | --- | --- | --- |
| SPV.0060. | Cross Stitching Longitudinal Cracks | EACH | EACH |