Complete (

# Concrete Sidewalk, California Picture Frame (Inch)

SPV.0165.

905-_____-_____

#### Buy America

Certification documents for steel reinforcement items must denote compliance to all elements of Buy America provisions.

See Item of Concrete – Class II

- Assign 905-____-____

Dowel Bars

Steel

- Diary entry required.  Bid Item ID: _______________

  - Certified report of test and analysis are required

  - Buy America compliance from manufacturer is required

Epoxy

- Diary entry required.  Bid Item ID: _______________

  - Certified report of test and analysis are required

  - Buy America compliance from manufacturer is required

  - Verify manufacturer is on the approved list

Tie Bars

Steel

- Diary entry required.  Bid Item ID: _______________

  - Certified report of test and analysis are required

  - Buy America compliance from manufacturer is required

Epoxy

- Diary entry required.  Bid Item ID: _______________

  - Certified report of test and analysis are required

  - Buy America compliance from manufacturer is required

  - Verify manufacturer is on the approved list

Joint Filler

- Diary entry required.  Bid Item ID: _______________

| Item No. | Description | Plan Quantity | Final Quantity |
| --- | --- | --- | --- |
| SPV.0165. | Concrete Sidewalk, Picture Frame (Inch) | SF | SF |