Complete (

# Adjusting Sanitary Manhole Covers

SPV.0060.

905-_____-_____

See Item of Concrete – Class III

- Assign 905-____-____

Brick and Block

- Diary entry required.  Bid Item ID: _______________

  - Verify that the manufacturer is on the approved list:

Precast Concrete and Masonry – Unit concrete masonry and brick

  - Record identifying mark and/or color when applicable.

Mortar Joint Connection

Mortar Cement – Type S

- Diary entry required. Bid Item ID: _______________

  - Manufacturer’s certification of compliance is required.

  - Record percentage of components.

Portland Cement

- Diary entry required. Bid Item ID: _______________

  - Manufacturer’s certification of compliance is required.

  - Record percentage of components.

Masonry Cement – Type S

- Diary entry required. Bid Item ID: _______________

  - Manufacturer’s certification of compliance is required.

  - Record percentage of components.

Hydrated Lime

- Diary entry required. Bid Item ID: _______________

  - Manufacturer’s certification of compliance is required.

  - Record percentage of components.

Bagged Utility Mortar

- Diary entry required. Bid Item ID: _______________

  - Verify product is on the approved products list:

Precast Concrete and Masonry – Prepackaged utility mortar

  - Ensure bags have label matching approved products list.

Mortar Sand

- Diary entry required. Bid Item ID: _______________

  - Sample in accordance with CMM 8-50 Exhibit 1, Mortar, Mortar Sand

Water

- Diary entry required. Bid Item ID: _______________

  - Record clarity of water.

Concrete Adjustment Rings

- Diary entry required.  Bid Item ID: _______________

  - Verify that the manufacturer is on the approved list:

Precast Concrete and Masonry – Precast concrete fabricators

  - Record identifying mark and/or color when applicable.

Adjustment Rings

- Diary entry required.  Bid Item ID: _______________

  - Verify that the manufacturer is on the approved list:

Precast Concrete and Masonry – Manhole adjustment products

| Item No. | Description | Plan Quantity | Final Quantity |
| --- | --- | --- | --- |
| SPV.0060. | Adjusting Sanitary Manhole Covers | EACH | EACH |